## Slide 1: Week 6- Lecture 3
Microprocessor Systems and Interfacing CPE 342

## Slide 2: ADC080X Analog-to-Digital Converter
A common, low-cost ADC, compatible with a wide range of microprocessors.
-While there are faster ADCs available with more resolution, this device is ideal for applications that do not require a high degree of accuracy
ADC080X requires up to 100 μs to convert an analog input voltage into a digital output code.
To operate the converter, the WR pin is pulsed with CS grounded to start the conversion process.

## Slide 3: ADC080X Analog-to-Digital Converter
timing diagram shows the interaction of the control signals.
If a time delay is used that allows at least 100 μs of time, there is no need to test INTR pin.
Another option is to connect the INTR pin to an interrupt input, so when the conversion is complete, an interrupt occurs.

## Slide 4: ADC080X Analog-to-Digital Converter
Before ADC0804 can be connected, the two analog inputs must be understood:
VIN(+) and VIN(–)
These differential inputs are summed by the operational amplifier to produce a signal for the internal analog-to-digital converter.
These inputs are connected to an internal operational amplifier

## Slide 5: ADC080X Analog-to-Digital Converter
Generating the Clock Signal: ADC0804 requires a clock source to operate.
It can be an external clock applied to CLK IN pin or can be generated with an RC circuit.
  permissible range of clock frequencies is 100KHz-1460 KHz.
  desirable to use a frequency as close as possible to 1460 KHz so conversion time is minimized
If generated with an RC circuit, CLK IN and CLK R pins are connected to an RC circuit

## Slide 6: ADC080X Analog-to-Digital Converter
ADC0804 interfaced to an 8086
  VREF is not attached to anything, which is normal

## Slide 7: ADC080X Analog-to-Digital Converter
ADC0804 interfaced to an 8086

## Slide 8: Using the ADC0804 and the DAC0830
This illustrates an example using an ADC0804 and a DAC0830 to capture and replay audio signals or speech.
A speech synthesizer has been used in the past to generate speech, but quality was poor
For human quality speech, we can use an ADC0804 to capture an audio signal and store it for later playback through a DAC0830.

## Slide 9: Using the ADC0804 and the DAC0830
Address Decoder 20 H